## Slide 1: 2025 Nova Lake CRD_ODM Summary Report
Rev2.0, CQ&R CMEE Team, 2025Q4
Stop
Customers confidential information under NDA, Intel internal use only

## Slide 2: General SMT Line Layout
Solder Paste Inspection (SPI)
Pre-Reflow Automated Optical Inspection (AOI) - Optional
Post-Reflow Automated Optical Inspection (AOI)

## Slide 3: Objectives
Data Collected From 8 ODM Customers/Sites
  Compal (Kunshan – Build for Dell/HP/Lenovo)
  Huaqin (Build for Huawei/Asus/Lenovo/Samsung)
  Inventec Chongqing (Build for HP/Asus)
  LCFC (Build for Lenovo)
  MSI KunShan (Own Brand)
  Pegatron (Suzhou - Build for Microsoft, Chongqing – Build for Asus)
  Quanta (Chongqing – Build for HP)
Share Findings From CMEE Mobile Industry Data Collection (Nova Lake Platform Customer Survey)

## Slide 4: Agenda
MOB
MOP and POP
Adhesive
Machine
Pick & Place (miniaturization - TK3)
Recycled Solder Paste
SMT Process
Stacked Capacitor
Rework
MOP & POP Test Related

## Slide 5: Highlights
For MoB design, all customers use Hardware strap to deliver correct memory configuration to BIOS.
5/8 customers(LCFC, Huaqin, Inventec CQ, Pega SZ and Compal KS) have MoP or PoP memory dipping experience.
Customers don’t monitor the X-ray dosage on the memory during X-ray inspection.
All customers don’t have any pre-SMT or post-SMT top-side die geometric (flatness, parallelism, etc.) expectations.
Most customers apply adhesive before function test. If adhesive must be done after function test, production line layout update is their main concern.
Most customers’ software can not detect and inspect flux dipping quality when flux is transparent.
Only Huaqin, Pegatron SZ and Compal KS have experience on 01005 passive component.
LCFC and Pegatron SZ have experience on recycled solder paste. SJ quality and reliability are customers’ main concern.
LCFC, Huaqin, Inventec CQ and Compal KS have PoP package rework experience, but no customers has experience of memory replacement with edge or corner glue.
Most customers have Debug POST card at their debug station.

## Slide 6: MOB Related

## Slide 7: MOB(1 Of 2)
For MOB design, all customers use Hardware strap to deliver correct memory configuration. to BIOS
 | Do you have memory on board (MoB) design? | If yes, please specify the pitch and the memory ball size. | In MoB (Memory on Board) design, correct memory configuration information (memory supplier, capacity, speed etc) must be deliver to BIOS, otherwise the board cannot boot. In your MoB design, what is the mechanism you use to deliver correct memory configuration to BIOS?
LCFC | Yes | Pitch: 0.75mm; Ball size: 0.45mm | Hardware strap
Huaqin | Yes | Pitch: 0.8mm; Ball size: 0.41mm | Hardware strap
Inventec CQ | Yes | Pitch:0.7 mm; Ball size: 0.4 mm | Hardware strap
MSI | Yes | Pitch:0.76 mm; Ball size: 0.26 mm | Hardware strap
Pega SZ | Yes | Pitch:0.7 mm; Ball size: 0.41 mm | Hardware strap
Compal KS | Yes | Pitch:0.4 mm; Ball size: 0.21 mm | Hardware strap
Quanta CQ | Yes | Pitch:0.7 mm; Ball size: 0.41 mm | Use software to check
Pega CQ | Yes | Pitch:0.7 mm; Ball size: 0.3 mm | Hardware strap

## Slide 8: MOB(2 Of 2)
Customers have very high memory chip FPY. Few customers apply adhesive on memory.
 | For MoB design, what is the memory chip first pass yield(include SMT and functional failure)? | For MoB design, what is the memory reliability field return rate? | For MoB design, do you apply adhesive on memory? | If yes, what adhesive do you use?
LCFC | ＜500ppm | No information from factory | Yes | Underfill
Huaqin | 100 DPPM | 0.05% in 2 years | Only if customer required | Corner glue
Inventec CQ | 180 DPPM | No information from factory | Yes | Corner glue
MSI | 153 DPPM | No information from factory | No | NA
Pega SZ | <100 DPPM | Almost no failure | No | NA
Compal KS | <1000 DPPM | No information from factory | No | NA
Quanta CQ | Almost no failure | No information from factory | Depends on customer requirement, most customer don't require adhesive on memory | Corner glue
Pega CQ | 500 DPPM | No information from factory | No | NA

## Slide 9: MOP and POP Related

## Slide 10: MOP and POP(1 Of 5)
LCFC, Huaqin, Inventec CQ, Pega SZ and Compal KS have MoP or PoP experience.
 | Do you have memory on package (MoP) or Package on Package (PoP) experience? | Are you capable for memory dip and placement on MoP (Memory on Package) or Package on Package (PoP)? | If yes, what is your PnP machine and dipping module model number you currently have? | If yes, what is the model number and manufacturer of dipping flux or dipping paste you are using? | If using paste, please specify the formulation type and mesh size
LCFC | Yes | Yes | PnP Machine: Panasonic NPM-TT2 POP feeder: N610095856AA | FLUX: Senju NSV301HF(BK)-AX FLUX: Shenmao SMBF-08 | NA
Huaqin | Yes | Yes | PnP Machine: NPM D3. Dipping module: N610095856AB | Indium,SAC305/TYPE5-MC/INDIUM988HF/80% | Type5
Inventec CQ | Yes | Yes | PnP Machine: NPM-D3A POP Feeder: N610056362AA | Shenmao: PF606-XP26 | Type6
MSI | No | No | NA | NA | NA
Pega SZ | Yes | Yes | PnP Machine: NPM dipping module: PANA Dipping Unit | Supplier: Alpha, Type: POP33 | Type5
Compal KS | Yes | Yes | Panasonic NPM-DX | Customer not answered | Customer not answered
Quanta CQ | No | No | NA | NA | NA
Pega CQ | No | No | NA | NA | NA

## Slide 11: MOP and POP(2 Of 5)
 | For MoP, do you prefer dipping flux or dipping paste ? | Could you help to explain the reason? | What is the minimum KOZ your equipment is capable of for adhesive dispense? | Does your adhesive dispense process capable of apply adhesive within 1mm KOZ (Keep Out Zone) from the package edge?
LCFC | Dipping flux | Dipping flux is more easy, high yield rate | 1 mm | Yes
Huaqin | Dipping paste | 1. Easy to check the dipping height 2. Easy to soldering, less open failure | 2mm | Yes, but the operation has risk
Inventec CQ | Dipping paste | Easy to soldering, less open failure | 1.2 mm, adhesive sparking on the CPU | No, minimum is 1.2 mm
MSI | Dipping flux | Short risk | 2mm | No
Pega SZ | Dipping flux | Use dipping flux for small pitch part, use dipping paste for big pitch part | 2mm | No experience, need to test
Compal KS | Dipping flux | Customer not answered | 1.5mm | No experience, need to test
Quanta CQ | No preference, Taiwan use dipping paste, Shanghai use dipping flux | Customer not answered | 1.5mm | No
Pega CQ | NA | NA | 1.5mm | No

## Slide 12: MOP and POP(3 Of 5)
Most customers use X-ray to inspect PoP or MoP solder joints
 | What is minimum KOZ you needed, to rework/replace a memory chip? | What is the most common PoP or MoP inspection technique for solder joints after placement and reflow? | Is this 100% inspection for HVM? | If not, what is the inspection requirement?
LCFC | 1mm | X-ray | No | 2 pcs/2 hrs
Huaqin | 1mm | X-ray | No | 1%
Inventec CQ | 2mm | X-ray | No | 1 Pc/2 hours
MSI | 2mm | NA | NA | NA
Pega SZ | 1mm | X-ray | No | Depends on yield, 20% at least
Compal KS | 1mm | X-ray | No | 5 pcs/shift
Quanta CQ | 1mm | NA | NA | NA
Pega CQ | 1.5 mm – 2 mm | NA | NA | NA

## Slide 13: MOP and POP(4 Of 5)
Customers don’t monitor the X-ray dosage on the memory during X-ray inspection.
Customers have no experience on Board Flexure analysis for MoP package.
 | For the Memory On Board design, do you monitor the X-ray dosage on the memory during X-ray inspection? | How do you currently perform Board Flexure analysis for a SOC, with a PoP or MoP device mounted on top of the SOC?
LCFC | No | No
Huaqin | No | Yes, no difference
Inventec CQ | No | No
MSI | NA | NA
Pega SZ | Depends on customer requirement | Yes, no difference
Compal KS | No | Yes, no difference
Quanta CQ | NA | NA
Pega CQ | NA | NA

## Slide 14: MOP and POP(5 Of 5)
All customers don’t have any pre-SMT or post-SMT top-side die geometric (flatness, parallelism, etc.) expectations.
 | Do you have any geometric (flatness, parallelism, etc.) expectations for pre-SMT or post-SMT top-side, e.g. die? | If yes, what is the geometric expectation？ | If yes, how is it measured? | If yes, does every component get measured or just some sampling of units during development? | If yes, are there different expectations for MOP? Please explain.
LCFC | No | NA | NA | NA | NA
Huaqin | No | NA | NA | NA | NA
Inventec CQ | No | NA | NA | NA | NA
MSI | No | NA | NA | NA | NA
Pega SZ | Depends on customer requirement | No spec, only for thermal solution design | OMM/CMM | Only in NPI | NA
Compal KS | No | NA | NA | NA | NA
Quanta CQ | No | NA | NA | NA | NA
Pega CQ | No | NA | NA | NA | NA

## Slide 15: Adhesive Related

## Slide 16: Adhesive(1 Of 5)
Most customers apply adhesive before function test. If adhesive must be done after function test, production line layout update is their main concern.
GKG and AXXON are the most popular in industry.
 | Do you apply adhesive before or after board level functional test? | If adhesive must be done after functional test, what is the impact? | What is your adhesive Equipment Vendor? | What is your Model of Adhesive Equipment
LCFC | Before function test | Production layout need to change | AXXON | Ai100
Huaqin | Before function test | 1. Production layout need to change 2. Need more fixture, increase handling risk | GKG | GKG DH5-E
Inventec CQ | Before function test | Production layout need to change | GKG/HTD | GKG-D510/HTD-420
MSI | Before function test | 1. Production layout need to change 2. Need more fixture, increase handling risk | AXXON | AI100
Pega SZ | Both | Component under shield cap must be glued before RF test | ANDA, AXXON | AD-16-SWH3 AU77S
Compal KS | Before function test | Production layout need to change | GKG | GKG-DH5
Quanta CQ | Before function test | Production layout need to change | Elite Automation | EM5701N
Pega CQ | Before function test | Production layout need to change | AXXON | AU99

## Slide 17: Adhesive(2 Of 5)
 | What is your Model of Valve | What is your Type of Valve | What is your Dispense Method
LCFC | APJ1000S | Piezo Jetting | Non-Contact Jetting
Huaqin | G3000K | Jetting | Non-Contact Jetting
Inventec CQ | Customer not answered | 1. Jetting; 2. Auger; | Non-Contact Jetting, Contact Auger
MSI | APJ1000S | Piezo Jetting | Non-Contact Jetting
Pega SZ | AD-16-SWH3---PS8600 AU77S---APJ1000 | Jetting, Time-pressure and Piezo Jetting | Non-Contact Jetting
Compal KS | 300H | Piezo Jetting | Non-Contact Jetting
Quanta CQ | GE3200K | Piezo Jetting | Non-Contact Jetting
Pega CQ | AXXON-V-6500 | Jetting | Non-Contact Jetting
All customers are capable for non-contact jetting dispense.

## Slide 18: Adhesive(3 Of 5)
 | What is your Nozzle Size(s) used / available | What is your Maximum Board Size (X & Y) to feed in your adhesive dispense machine? | What is your Maximum Board Height (Z) to feed in your adhesive dispense machine?
LCFC | Inner Diameter: 200um | 440mm*760mm | 6mm
Huaqin | Inner Diameter: 200um | 350 mmX550mm | 8mm
Inventec CQ | Inner Diameter：600um，Outer Diameter: 900um | 510 mm*510mm | 6mm
MSI | 400um | 440mm*760mm | 2mm
Pega SZ | AD-16-SWH3----250um AU77S----150um | AD-16-SWH3----340*500mm AU77S---350*475mm | 6 mm
Compal KS | 100um,150um,200um | 400*310mm | 6 mm
Quanta CQ | Inner diameter: 0.25mm | 350mm*450mm | 1.6 mm
Pega CQ | Inner diameter 0.4mm | 450mm*318m | 1.61mm

## Slide 19: Adhesive(4 Of 5)
Most customers use Valve or Nozzle Heating for Dispensing Adhesive and have programmable Multiple Z Height Capability in the same dispense task.
 | Do you use Valve or Nozzle Heating for Dispensing Adhesive | If yes, what is the temperature range? | Does your machine has programmable Multiple Z Height Capability in the same dispense task? | If yes, what is the Z height range?
LCFC | Yes | 20-80°C | Yes | 0 to 40mm
Huaqin | Yes | 20~150°C | Yes | 1 to 20mm
Inventec CQ | Yes | 40-55℃ | Yes | HTD -0.2_-0.5mm GKG 2-5mm
MSI | Yes | 30-70°C | Yes | 0 to 45mm
Pega SZ | Yes | 20-100°C | Yes | 0 to 20mm
Compal KS | Yes | 20~80°C | Yes | 40-100mm
Quanta CQ | Yes | 20-80℃ | No | NA
Pega CQ | No | NA | No | NA

## Slide 20: Adhesive(5 Of 5)
 | Could you provide the Equipment Datasheet (if possible)? | Do you perform X-Y Calibration? | What is your X-Y Accuracy? | Do you perform Z-Height Calibration? | What is your Z-Height Accuracy?
LCFC | Confidential | Yes | Positional Accuracy：±50um@3σ | Yes | :±10um@3σ
Huaqin | Yes | Yes | ±15um@4sigma(CPK>1.33) | Yes | ± 30um@4sigma(CPK>1.33)
Inventec CQ | Yes | Yes | ± 30um | Yes | ± 30um
MSI | Confidential | Yes | +/-50um | Yes | +/-50um
Pega SZ | Yes | Yes | +/-10um | Yes | +/-10um
Compal KS | No | Yes | +/-30um | Yes | +/-30um
Quanta CQ | No | Yes | ± 0.2mm | Yes | ± 0.2mm
Pega CQ | Yes | No calibration | ± 0.2mm | Yes | ± 0.2mm

## Slide 21: Machine Related

## Slide 22: Machine(1 Of 3)
 | Does your PNP tool have a high resolution upwards looking camera ? | If yes, what is the resolution (um/pixel and FOV in mm or Other specification) and Manufacturer/Camera Model number | Can your software detect and inspect flux dipping quality on BGA balls (good coverage, insufficient, bridging) when flux is transparent? | If No, do you require flux to be colored ?
LCFC | Yes | SHOWA: MTNG000492AA 9um @ ≤0402；18um @ ≥0603 | No | Yes
Huaqin | Yes | Panasonic, 18um/pixel | No | Yes
Inventec CQ | Yes | Original camera from NPM | Yes | No
MSI | Yes | Fuji/BMP04CL | No | Yes
Pega SZ | Yes | Original camera from the PnP machine | No | Yes
Compal KS | Yes | MUL TI-RECOGNITION CAMERA UNIT (TYPE1) MTKA005537AA | No | Yes
Quanta CQ | Yes | Original camera from NPM | No experience | No experience
Pega CQ | Yes | Fuji/P04CL | Yes | NA
Most customers’ software can not detect and inspect flux dipping quality when flux is transparent.

## Slide 23: Machine(2 Of 3)
 | Does the PNP dipping tray have flux height control ? | If yes, how height is initially set up and periodically checked (after how many dip operations, it is re-checked) | For a given BGA solder ball that has a height of 0.145 mm, ball dia 0.215 and ball pitch of 0.35 mm, what is the desired dipping flux control height? | What is the minimum spacing distance in mm required for placing 2 DRAM BGA packages side by side?
LCFC | Yes | 1 check/2 hours | Dipping height：50-70% Ball height | 0.7mm @LNL DOE
Huaqin | Yes | 1 check/1 hour | 0.08mm，60-80% Ball height | 0.5mm
Inventec CQ | Yes | 1 check/2 hours | 0.07 mm, 50% Ball height | 2mm
MSI | NA | NA | NA | 1mm
Pega SZ | Yes | 1 time/2 hours | No experience, need to test | No experience, need to test
Compal KS | Yes | 1 check/1 hour | 40%-50% Ball height | 1 mm
Quanta CQ | No experience | No experience | No experience | 3mm
Pega CQ | Yes | 2 times/shift | Flux dipping depth is 50~70% of solder ball height, so it is 0.07~0.1mm | 2mm

## Slide 24: Machine(3 Of 3)
 | Do you have AXI machine? | If yes, what is the machine maker and model? | If yes, does the machine is online of offline? | If you have PoP projects before, do you use AXI machine to inspect MLI joints? | If no, does your 2D X-ray machine has automatic inspection feature?
LCFC | No | NA | NA | No | No
Huaqin | No | NA | NA | NA | No
Inventec CQ | No | NA | NA | Use manual X-ray | Yes
MSI | No | NA | NA | NA | NA
Pega SZ | No | NA | NA | NA | NA
Compal KS | No | NA | NA | NA | No
Quanta CQ | No | NA | NA | Use manual X-ray | NA
Pega CQ | No | NA | NA | Use manual X-ray | No
All customers don’t have AXI machine.

## Slide 25: Pick & Place (miniaturization - TK3)

## Slide 26: Pick & Place (miniaturization - TK3)
 | Do you use 01005 passive component in your HVM product? | If yes, what is your typical challenges? | If no, is 0201 the smallest passive component used?
LCFC | No | Material cost, design requirement, manufacturing yield | Yes
Huaqin | Yes | The PCB warpage will lead printing and PnP skew issue | NA
Inventec CQ | No | NA | Yes
MSI | No | No needs | Yes
Pega SZ | Yes | Need special feeder | NA
Compal KS | Yes | Short risk | NA
Quanta CQ | No | Difficult to rework | Yes
Pega CQ | No | Too small | Yes
Only Huaqin, Pegatron SZ and Compal KS have experience on 01005 passive component.

## Slide 27: Recycled Solder Paste

## Slide 28: Recycled Solder paste
 | Have you implemented recycled solder paste or solder bar in your product to support sustainability efforts? Opportunities to reduce PCBA Carbon Footprint >80% CO2 emissions | If yes, which solder paste supplier or model are you using or would prefer to use? | If no, what is the primary reason for not considering recycled solder paste or bar? | If no, what data would be needed to start using recycle solder paste on some percentage of your products?
LCFC | Yes | Senju M705R | NA | NA
Huaqin | No | NA | Solder joint quality | SJR, SJQ data, cost parity to SAC, supply availability
Inventec CQ | No | NA | No requirement from customer | NA
MSI | No | NA | SJ quality, reliability | We don't consider recycle solder paste
Pega SZ | Yes | Senju M705R | NA | NA
Compal KS | No | NA | Printing issue | SJR, SJQ data, cost parity to SAC, supply availability.
Quanta CQ | No | NA | All solder paste was requested by customer | Depends on customer requirement
Pega CQ | No | NA | SJ quality, reliability | SJR
LCFC and Pegatron SZ have experience on recycled solder paste. SJ quality and reliability are customers’ main concern.

## Slide 29: SMT Process

## Slide 30: SMT Process Related(1 Of 4)
 | What is the minimum board thickness you have supported? | What is your typical challenges for building a 0.6 mm thick PCB? | What is the minimum component(0201 or 0402 chip) spacing on your product?
LCFC | 0.6 mm | Warpage issue | 0.178mm(7mil)
Huaqin | 0.4 mm - small board only | The PCB warpage will make the printing, PnP and soldering process are unstable | 0201:0.2mm；0402:0.25mm
Inventec CQ | 0.4 mm- small board only | Warpage | 0.15mm (6mil)
MSI | 0.8 mm | Yes, The warpage will make the part easy to crack after soldering | 0.23mm
Pega SZ | 0.4 mm- small board only | Board warpage issue | 0.15mm
Compal KS | 0.7mm | Yes, warpage issue, assembly issue | 0.25 mm
Quanta CQ | 0.7mm | Easy to deform | 0.2mm
Pega CQ | 0.6mm | Warpage | 0.2mm(8mil)
For building a 0.6 mm thick PCB, warpage is customers’ main concern.

## Slide 31: SMT Process Related(2 Of 4)
 | Do you have experience with 0.10mm (4mil) component spacing for small component such as 0201/0402 to small QFN/BGA ( 4mm x 4mm body size) | If No, would you consider doing this for your product? | If No, what is your concern?
LCFC | No | No | SMT yield
Huaqin | No | No | Too close to the BGA, the part tolerance may interfere the printing process
Inventec CQ | No | No | Customer not answered
MSI | No | No | Yield and rework
Pega SZ | No | No | 1.Stencil will cause printing issue 2. Interference during PnP process
Compal KS | No | No | Printing issue, shortage
Quanta CQ | No | No | PnP issue, difficult to rework
Pega CQ | No | No | Printing and PnP issue

## Slide 32: SMT Process Related(3 Of 4)
 | What is the minimum pitch for any device used on your product? QFN, SMT connector or BGA | What is the maximum EMI shield size you experience?
LCFC | 0.35 pitch BGA (MTK PoP) | 100mm*90mm
Huaqin | 0.3 mm | 80mm*16mm
Inventec CQ | 0.35mm | 90mm*40mm
MSI | 0.35mm | NA, use clip
Pega SZ | 0.35mm | >100mm*100mm
Compal KS | 0.3 mm - 0.35 mm | 100mm*50mm
Quanta CQ | 0.35mm | 60mm*60mm
Pega CQ | 0.3mm | 70mm*30mm

## Slide 33: SMT Process Related(4 Of 4)
 | Have you used step EMI shield before? | If yes, what is the challenges you face? | Do you normally build 2 or more different boards within the same panel? These boards will be used to assemble into a system later in the process. | If yes, what are the challenges? Please explain
LCFC | No | NA | Yes | No
Huaqin | No | NA | Yes | No
Inventec CQ | No | NA | Yes | Sometimes have traceability issue
MSI | No | NA | Yes | No
Pega SZ | Yes | 113*113cm, flatness issue | Yes | No
Compal KS | No | NA | Yes | No
Quanta CQ | No | NA | Yes | No
Pega CQ | No | NA | Yes | No
Only Pegatron SZ has experience on step EMI shield. All customers have experience on building 2 or more different boards within the same panel.

## Slide 34: Stacked Capacitor

## Slide 35: Stacked Capacitor Related (1 Of 2)
 | Have you use stacked capacitor in your product? | Do you see the value for stacking the Cap in your product? | Would you prefer the Cap pre-stacked by supplier or develop a factory stacked using SMT process. | Would you have interest for Intel to share the new pre-stacked cap SMT concept with you?
LCFC | No | No answer from customer | No answer from customer | Base on design requirement
Huaqin | No | Yes, this design can reduce board size | Pre-stacked | Yes
Inventec CQ | No | No | Pre-stacked | Yes
MSI | No | No | Pre-stacked | Yes
Pega SZ | No | No design requirement | Pre-stacked | Yes
Compal KS | No | No answer from customer | Pre-stacked | Yes
Quanta CQ | No | No | Pre-stacked | Yes
Pega CQ | No | No | Pre-stacked | Yes
All customers never used stacked capacitors and they prefer pre-stacked by supplier.

## Slide 36: Stacked Capacitor Related(2 Of 2)
 | Paste Jetting – Do you have paste jetting capability? | If yes, in what application do you use it? | If paste jetting machine is required for stacked Cap SMT process, would this be a show stopper for implementing concept? | Reflow – Is a 3rd reflow cycle a concern for implementing the stacked Cap concept? | If yes, why?
LCFC | Yes | Not used anymore | NA | No answer from customer | No answer from customer
Huaqin | No | NA | No | Yes | Cost, reliability
Inventec CQ | No | NA | Yes | Yes | Cost
MSI | No | NA | No | Yes | Quality, reliability
Pega SZ | No | NA | Depends on customer requirement | May have influence on the BGA | Quality, reliability
Compal KS | Yes | MTL-M | NA | Yes | Reliability
Quanta CQ | No | NA | Depends on customer requirement | Yes | Line layout update, cost
Pega CQ | No | NA | Depends on customer requirement | Yes | Cost, reliability
Only LCFC and Compal KS have paste jetting capability.

## Slide 37: Rework

## Slide 38: Rework Related(1 Of 3)
 | What equipment vendor do you use for automated rework? | What model of equipment do you use for automated rework? | What mode of heating does your tool use? | What is the largest BGA package you have successfully reworked?
LCFC | DIC | RD500-V | Combination | 50mmX25mm
Huaqin | Ersa | Ersa Hybrid Rework 600 | Combination | 50mmX25mm
Inventec CQ | Yeou Electric(local brand) | BTF-950 | Convection | 50mmX25mm
MSI | Microasm | MLX- E6250C | Combination | 41.5mm x41.5mm
Pega SZ | VTTECH, SRT | 360SAM | Convection | 52mm*52mm
Compal KS | QUICK | EA-H15 | Infrared | 50mm*31mm
Quanta CQ | QUICK | EA-H00 | Convection | 50mmX25mm
Pega CQ | DIC, Quick | RD500III RD500S III | Combination | 50mmX25mm

## Slide 39: Rework Related(2 Of 3)
 | What is the thickest board you are capable of reworking | Have you successfully reworked Package on Package? | Do you use specialized collaterals for Package on Package rework, and if so, please list | Have you successfully reworked packages with edge or corner glue?
LCFC | 1.6 mm | Yes | Scraper Tool, PCBA pallet, customized nozzel | In study @LNL MOP
Huaqin | 1.6 mm | Yes | Customized fixture, rework station | No
Inventec CQ | 1.6 mm | Yes | Site heater | No
MSI | 1.6 mm | No | Site heater | No
Pega SZ | 1.78mm | Yes | Flux | No
Compal KS | 1.6 mm | NA | NA | NA
Quanta CQ | 1.6 mm | NA | NA | NA
Pega CQ | 1.27 mm | NA | NA | NA
LCFC, Huaqin, Inventec CQ and Compal KS have successfully reworked PoP package, but all customers have not successfully reworked packages with edge or corner glue.

## Slide 40: Rework Related(3 Of 3)
 | What is your preferred rework method to replace memory on package on package? | What is your method of reflashing BIOS when repairing a failing board? 1. Remove and replace SPI Chip 2. Reflash the BIOS using EFI or WinOS tool (ie. FPT- Flash Programmable Tool) 3. Both #1 and #2 | Do you have Debug POST card? | If yes, how many card do you usually have in your repair station?
LCFC | Flux brushing, automatic placement | Both | Yes | 1pc/Person
Huaqin | Automatic placement | Both | Yes | 1pc/Person
Inventec CQ | Flux brushing | Both | Yes | 1pc/Person
MSI | Automatic alignment and placement | Both | Yes | 1 card/station, typec and HDMI
Pega SZ | Manual placement and alignment | Both | No, use SAM/UEFI log file, output from debug port | NA
Compal KS | Flux brushing, automatic placement | Both | No | NA
Quanta CQ | Customer not answered | Remove and replace SPI Chip | Yes | Not used now
Pega CQ | Prefer automatic placement, but current machine does not support this function | Both | Yes | 1 card/station
Most customers have Debug POST card at their debug station.

## Slide 41: MOP & POP Test Related

## Slide 42: MOP & POP Test Related(1 Of 1)
 | Does your SMT implement ICT or ATE test? | If yes, only ICT or ATE or Both? | If yes, do you cover power signal test related to memory? | If yes, do you cover memory data signals? | If yes, do you cover boundary scan test on memory data signals?
LCFC | Yes | ICT ATE | No | No | No
Huaqin | Yes | ICT | No | No | No
Inventec CQ | Yes | ICT | No | No | No
MSI | Yes | ICT | No | No | No
Pega SZ | Yes | Only FCT | NA | NA | NA
Compal KS | Yes | ATE | Yes | No | No
Quanta CQ | Yes | ICT | Yes | Yes | Yes
Pega CQ | Yes | ICT desktop/notebook MDA | No | No | No