## Slide 1: 2025 Mobile CRD SEA ODM Summary Report
Rev1.0, CQ&R CMEE Team, 2025Q4
Stop
Customers confidential information under NDA, Intel internal use only

## Slide 2: General SMT Line Layout
Solder Paste Inspection (SPI)
Pre-Reflow Automated Optical Inspection (AOI) - Optional
Post-Reflow Automated Optical Inspection (AOI)

## Slide 3: Highlights
We total surveyed 5 SEA customers – Compal VN, LCFC VN, Wistron VN, Quanta TH and Inventec TH, received response from 4 customers, Wistron did not response
SEA ODMs are copying exactly from their PRC site
The volumes are ramping up, eventually could > 50% of ODM shipping volume
  Currently the line efficiency still not compare-able to PRC site, it will be improved with the maturity of local site
At LCFC VN and Inventec TH almost all engineers are still Chinese, didn’t see local engineer
Compal VN and Quanta TH are better on localization, saw ~50% of the meeting attendees are local engineer

## Slide 4: Factory Set Up
LCFC does not have system assembly at VN yet, other customers can do system assembly at local
 | How many SMT lines do you have now? | Do you perform both motherboard SMT and final System Assembly operations? Do post-SMT motherboards have to transfer to another factory for final System assembly? | What is your daily or weekly output capacity?
Compal VN | 12 | In house system assembly | 120K/week
LCFC VN | 11 | 1. Send MB LCFC HF； 2. Send to Luxshare No local system assembly so far | 125K/week
Inventec TH | PSG ITH01-SMT MB*2; PSG ITH02-SMT MB*5, DB*2 | In house system assembly | 58K/week
Quanta TH | 10 | 1. Send MB Quanta CQ； 2. Local assembly | 300K/week

## Slide 5: BGA Handling, Moisture and ESD
 | Are you aware of, and do you follow Intel's BGA package handling recommendations, as found in the Intel Product Transport and Media Handling MAS (RDC# 619185)? | Do you have robust factory processes and controls to track and mitigate over-exposure moisture levels, to accommodate Intel's MSL 3 BGA components? (please describe) | Do you have robust factory processes to mitigate ESD/EOS issues with Intel's BGA components? (please describe)
Compal VN | Yes | 1. Temperature and humidity control in factory floor 2.Record MBB back open time, bake the component if expire MSL time | 1.Everyday measure ESD shoes, solder irons, electric screwdriver 2. Every week measure working tables/benches, shelves, ESD bags, equipment 3.Every Quarter measure working floor, Ionizers, conveyors, carts 4. ESD wrist strip real time monitor and alert
LCFC VN | Yes | 1. Before send into warehouse a. Check package no damage, confirm MSL level, date code information on package label b. Store the MBB bag in controlled environment (Temp：18-27°C, Humidity30- 60% RH） 2. After MBB open a. Check HIC card b. Record MBB on time at system, print/paste control label on package 3. Tracking system a. System set up to control moisture and expire time (ex. MSL 3 = expire at 168 hrs) b. automatic record open time, expire time, status, reminder operator to deal with the about-to-expire parts c. Barcode system: Every batch is unique barcode to tracking the status and history | Yes we have comprehensive ESD/EOS control process to control fixtures/equipment/packing material and operators. All employees had be trained and will regular retrain and exam In production line people must wear ESD Smock, shoes and wrist strap. Regularly test grounding system. Key station equipped with ionizers, ESD mat. Material packed with anit-ESD bags and cartons. Established EOS protection protocols, control power and signal inputs, regularly calibration
Inventec TH | Yes | Yes | Yes
Quanta TH | Yes | 1. BGA issue to production line according to build order, so no extra parts need to return after build. 2. After MBB open BGA will store in dry cabinet 3. Temperature and humidity control on production floor 4. Un-used BGA will be repacked with MBB and desiccant then return to warehouse | Yes 1. All equipment are grounded 2. Test station has ionizers 3. Operator must pass ESD test before can enter production floor

## Slide 6: Incoming Motherboard Inspection
All customers have certain level of PCB design check to align with Intel Land Pattern recommendation
 | Do you perform factory motherboard quality inspections to check they meet the specific Intel SOC Land Pattern Design Guidance (as shown in the Platform MAS)? | Do you perform factory motherboard quality inspections, to check that the minimum SRO on MD and spoked pads are followed by the PCB fabricators, to maintain sufficient clearance for solder flow (as shown in the Platform MAS)?
Compal VN | Yes, we have DFX department to confirm the pad design aligned with Intel recommendations | DFB team will do the verification
LCFC VN | We don't have PCB pad inspect equipment in factory. To make sure our pad design align with Intel recommendation, we ask PCB supplier to provide test report for each lot to make sure the key parameters (pad size, pitch, SRO size etc) followed our Gerber design and Intel recommendation | We don't have PCB pad inspect equipment in factory. To make sure our pad design align with Intel recommendation, we ask PCB supplier to provide test report for each lot to make sure the key parameters (pad size, pitch, SRO size etc.) followed our Gerber design and Intel recommendation
Inventec TH | Yes | YES， 1.RD will refer to Intel MAS design 2.During the trial production process, when problems occur, the process engineer will refer to Intel MAS for inspection!
Quanta TH | During NPI build ME will work with RD to make sure BGA pad (ex, SMD, non-SMD, Spoked Pad etc.) followed Intel MAS recommendations | compare with film

## Slide 7: Solder Paste (1/2)
SEA ODMs use the same solder paste material and printing machines as their China sites. More ODM start to use GKG machine
 | What is the SAC solder paste you are using now? List all the solder pastes brand and model# you are using | When building with Intel BGAs, are you able to use one of the Intel-Evaluated solder pastes in the list (as shown in the Platform MAS), to minimize the amount of SMT defects? | What is the paste print machine you are using? List all the print machine brand and model# you are using
Compal VN | YunNan Tin and ShenMao PF606, SAC305 | Yes | GKG G+, G++
LCFC VN | ShenMao PF606 P（20-38μm) ShenMao PF606 P26（15-25μm） Senju M705-S101HF(NL3)-S4 Senju L29-155HF(L)Type4(J51) | Yes | GKG, GT++
Inventec TH | (500g)-Shenmao-PF606-P (SAC305) -Type4 (500g)-Tamura-TLF-204-93 IVT(SAC305) -Type4 (500g)-EUNOW-EUP-1000HQR(SAC305) -Type4.5 (500g)-YUNNAN TIN-YW9-3005-98CY04(SAC305) -Type4 (50g)--Shenmao-PF606-XP26 (SAC305) -Type6 POP | (500g)-Shenmao-PF606-P (SAC305) -Type4 (500g)-EUNOW-EUP-1000HQR(SAC305) -Type4.5 (500g)-YUNNAN TIN-YW9-3005-98CY04(SAC305) -Type4 | Panasonic NPM-GP-L New line A+B side） ASMPT DEK NeoHorizon 03iX (B side） GKG GT++ (A side）
Quanta TH | ShenMao PF606 | Yes, ShenMao PF606 | DEK/SPG2

## Slide 8: Solder Paste (2/2)
4 mil and 5 mil are still the major stencil thickness customer preferring.
Customer will follow Intel MAS first then do customization based on result
 | What is your preferred solder stencil thickness, when building with Intel BGAs? (e.g. 3 mil / 4 mil / 5 mil) | Are you able to follow all of Intel's solder stencil design recommendations (as shown in the Platform MAS), to minimize the amount of SMT defects? If not, please explain why. | Do you see any correlation between any specific solder pastes types/models that you use which cause a greater number of solder joint defects on Intel's BGAs?
Compal VN | 4mil | First revision 100% follow Intel MAS | Lunar Lake CPU, during NPI we found if use YunNan Tin will have big void, so we only use ShenMao Paste now
LCFC VN | 4mil, 5mil | Yes | No
Inventec TH | 4 mil （3mil Used under special circumstances） | The first build must follow Intel MAS, If abnormalities are found, local corrections will be made based on Intel MAS using Inventec know-how！ Localized concentrated SJR or Open , because the Warpage amount is mastered | YES， (500g)-Shenmao-PF606-P (SAC305) -Type4 (500g)-Tamura-TLF-204-93 IVT(SAC305) -Type4
Quanta TH | 0.08/0.1/0.12 MM (3/4/5mils) | Not 100%. We will do some modification per the real situation | No, we only use ShenMao PF606 now

## Slide 9: Solder Paste Inspection
 | What is your SPI machine brand and model? List all the SPI machine brand and model# you are using | What are your SPI inspections limits (upper volume / lower volume)?
Compal VN | Holly D686; JET, JET-600 | 60%~150%
LCFC VN | Truteck TU521, TU560 | 
Inventec TH | SinicTEK inSPIre-H510 (Single-track) SinicTEK inSPIre-H510B (dual-track) TRI 7007 SII TRI 7006 | 40%~160%
Quanta TH | TRI 7007 | 70%~150%

## Slide 10: PnP and PoP
All 4 ODM’s PnP machine are from Panasonic
 | What is the pick and place machine you are using? List all the PnP machine brand and model# you are using | Do you use 100% Ball Recognition for BGA placement? | Do you have PoP process capability? If yes, what method is used to check consistent flux heights. | If yes, can you provide the PoP flux or PoP paste brand and model#?
Compal VN | Panasonic NPM-DX, NPM-TT2, NPM-WX | Yes | No PoP capability | NA
LCFC VN | Panasonic NPM-D2, NPM-D3, NPM-D3A, NPM-TT2 | Yes | Yes 1. Test flux thickness when shift open 2 Test flux thickness every 0.5hr 3.PnP camera auto check flux dipping quality | PoP paste: ShenMao PF606-P26，Type 5
Inventec TH | Panasonic NPM-D3A, NPM-TT2 | Yes | Yes 1.Thickness gauge detection of FLUX thickness on POP dip plate 2.Spot check the height of flux under the magnifying glass | (50g)--Shenmao-PF606-XP26 (SAC305) -Type6 POP
Quanta TH | Panasonic NPM | Yes | No PoP process now | N/A

## Slide 11: Reflow (1/2)
 | What is the pre-reflow AOI machine you are using? List all the pre-reflow AOI machine brand and model# you are using | What reflow oven you are using? List all the reflow oven brand and model# you are using | What is the max and min zones your reflow oven has?
Compal VN | Holly LX640 JET JET-7300DM | HELLER 2943MK5 ERSA 3/26XL | 13 Zones
LCFC VN | Vitrox, V510i Juzte Storm II | Heller 2043MK, 2049MK | 13 Zones
Inventec TH | Holly LX520iL （TOP camera） VCTA-S820L TRI 7500 (DB Line) | RHEM VXP/VXS 13 zone （MB Line） RHEM VXP 835 11 zone （DB Line） | Max 13 zone , Min 11 zone
Quanta TH | TRI7700 | ERSA | 13 Zones

## Slide 12: Reflow (2/2)
Customer complain Intel recommend too many TC heads on BGA, they want Intel to soften the recommendation in MAS
 | Do you use N2 reflow? If yes, what is the O2 PPM? | Do you use a reflow pallet for all products? If Yes, what material is used (e.g. Aluminum, Durastone, etc…)? | Do you create the reflow profile by drilling holes through the motherboard & installing them directly into the BGA balls (one at the BGA center, and one in each of 2 corners, as shown in the Platform MAS)? If not, what process is followed?
Compal VN | Yes, O2 < 3000 PPM | All product reflow will use Aluminum pallet | Follow MAS recommendation
LCFC VN | Yes, O2 < 1000 PPM | All CPU side reflow will use Aluminum pallet | Follow MAS recommendation, 1 TC head at center of BGA, 2 heads at 2 BGA corners
Inventec TH | Yes, O2＜1000ppm | Use a reflow pallet Aluminum | Follow MAS recommendation
Quanta TH | Yes, O2 < 2000 PPM | PCB thickness > 1.6mm, no pallet. <1.6mm, use Aluminum pallet | Follow MAS recommendation, 1 TC head at center of BGA, We do not put TC head at BGA corners and edges

## Slide 13: Post Reflow Inspection
 | What is the post-reflow AOI machine you are using? List all the post-reflow AOI machine brand and model# you are using | Are you familiar with the purpose of Cu Core standoffs and are they excluded from your x-ray inspections (not considered solder joint defects)? | What is your x-ray machine brand and model#? | Are you able to identify the most common types of solder joint defects, such as Non-Wet Open (NWO), Head On Pillow (HoP), Solder Ball Bridging (SBB)? | What is the most common solder joint defects that you observe on Intel's BGAs? (e.g. NWO, HoP, SBB) (please explain)
Compal VN | Holly LX640 JET JET-7300DM | Yes | DAGE, XD7500 | Yes | Solder Bridge
LCFC VN | Vitrox, V510i Juzte Storm II | Yes | Nordson (DAGE) XD7500VR JADE PLUS | Yes | Non Wet Open
Inventec TH | Holly LX520iL (TOP camera) Holly LX520iL-D (TOP and BOT camera) VCTA-S820L | YES, Refer to Intel MAS for judgment | ITH01 X-eye SF160 ITH02 Nordson DAGE Quadra 5 pro | Yes | Head on Pillow, Non Wet Open (a small amount)
Quanta TH | No post-reflow AOI | Yes | Dage Q5 | Yes | Solder Open

## Slide 14: Test
 | Do you do ICT or ATE test after reflow? If yes, list the machine brand and model# of the test machine you are using
Compal VN | TERADYNE: TSHL52
LCFC VN | TERADYNE: TSH52
Inventec TH | ICT, TRI 8100LV TRI 8001 Max support 128*28=3,584 point
Quanta TH | TRI

## Slide 15: Adhesive
SEA ODMs use the same adhesive and dispense machine as their China site, most of them use Zymet 2625B because of Lunar Lake project
 | Do you apply adhesive on BGA components? If yes, please list the adhesive brand and model you are using | Please list you adhesive dispense machine brand and model | Are you able to remove/rework the adhesive that is applied to Intel BGAs? If yes, please explain your process. | Are you familiar with, and do you use, the Torlon material scraper tool to help with the removal of reworkable adhesive material without causing damage to the motherboard soldermask (as shown in the Platform MAS)? | What is the smallest KOZ you are able to dispense adhesive onto a BGA/CSP? (e.g. 0.7mm, 1mm, 2mm)
Compal VN | Somida: SMD3805; ZYMET: UA-2625-B | GKG: DH350-P | Heat to low temperature then use special tool to remove adhesive | Yes | 2*5.4mm
LCFC VN | ASEC: AS-391003 (corner fill) | AXXON: Ai100 | Not easy to remove, need use special tools: Use hot air gun to heat the corner fill location until solder melt, then use blade shove off | No | 2mm
Inventec TH | LOCTITE: 3619 Zymet: UA-2625-B | HTD-420-C SDEC-400DL | Heat to around 130 degrees Celsius and remove with tweezers | Evaluating | 2mm
Quanta TH | LOCTITE : 3705(UV), 3619 (Thermal) ZYMET: 2625 | AXXON: MT60 | Easy to remove, Hot air gun setting at 1700C to heat up then remove glue | No | 3mm

## Slide 16: Rework
Same rework machine as we saw in ODM China site
 | What is your BGA rework machine brand and model? | Does your BGA rework station have N2 protection capability? | For BGA rework, do you prefer a flux-only process or solder paste application process? (please explain the reason)
Compal VN | QUICK: EA-H15 | Yes | Pitch<0.4mm, use flux; Pitch >0.4mm, use solder paste
LCFC VN | DEN-ON: RD-500V | Yes | Solder paste, because have higher yield
Inventec TH | 重庆业欧电子 BFT-2000 | No | solder paste (Substrate Warpage)
Quanta TH | QUICK H15 | No | Solder paste

## Slide 17: Miscellaneous
Except Inventec TH, all other customer has in house SJ FA capability
 | Do you have LTS process capability? | If yes, list all the LTS paste brand and model# you are using | Do you have in-house solder joint x-section and DnP capability? | Do you perform strain gauge measurement in your factory, to identify any factory operations which might be high risk to cause BGA solderjoint cracking? | Do you take specific steps to minimize die damage risk on Intel's bare die BGAs (from thermal solution assembly / disassembly / repair / rework processes?) If yes, please explain.
Compal VN | Yes | Nihon: LTS B37 P611 D6 F21 15G | Yes | Yes | Use tool to handle the whole process, no manual handling
LCFC VN | Yes | Senju: L29-155HF(L)-Type4 | Yes | Yes | NA
Inventec TH | Yes | No mass production | ITH still setting up, estimate capability available at Mar'26 | Yes | 1.Place the side with CPU facing upwards 2.Limit tray (EVA)
Quanta TH | No | No | Yes | Yes | No answer